Spek Anchor

Spek anchor is one type of stockless anchors. Spek anchor is modified from the Hall anchor, whose core of anchor head is located in the center of the pin center line to the bottom. The structure of Spek anchor is characterized that there is anchor crown plate and reinforcing ribs at the anchor crown. Therefore, the anchor claw is easily to turn to the ground and has better stability. Moreover, when collecting the anchor, its flukes keep naturally upward and overturn immediately when touching the hull plate to avoid damaging the shell plating.

Product Detail

- Type: Spek Stockless Anchor

- Material: casting steel

- Nominal Weight: 210kg to 20000kg (Type SR), 100kg to 26000kg (CB711-95), 80kg to 20000kg (Type M)

- Application: marine ships

- Certificate: CCS,ABS,LR,GL,DNV,NK,BV,KR,RINA,RS etc.

Spek Anchor Type

- CB/T711-1995 Spek Anchor

- Type M Spek Anchor

- Type SR Spek Anchor

Note: our company is a professional marine anchor supplier. We can supply all variety of anchors to meet your different needs. Our anchors are approved by classification societies and get the certificates. If you’re interested in our products, please feel free to contact us. We’re sincere to cooperate with you.

CB711-95 Spek Anchor

CB711-95 Spek Anchor Drawing

Specification

| Nominal Weight (KG) | Size(mm) |
| --- | --- |
|  | A | B | C | D | F |
| 100 | 672 | 373 | 112 | 515 | 250 |
| 150 | 770 | 428 | 128 | 590 | 290 |
| 180 | 846 | 470 | 140 | 640 | 300 |
| 240 | 900 | 500 | 150 | 690 | 358 |
| 300 | 990 | 550 | 166 | 760 | 398 |
| 360 | 1065 | 600 | 180 | 828 | 431 |
| 420 | 1080 | 600 | 180 | 828 | 446 |
| 500 | 1170 | 650 | 196 | 900 | 446 |
| 570 | 1170 | 650 | 196 | 900 | 486 |
| 660 | 1260 | 700 | 210 | 962 | 486 |
| 780 | 1355 | 750 | 225 | 1032 | 547 |
| 900 | 1440 | 800 | 240 | 1100 | 573 |
| 1020 | 1530 | 850 | 252 | 1170 | 591 |
| 1140 | 1620 | 900 | 268 | 1240 | 620 |
| 1290 | 1710 | 900 | 268 | 1240 | 640 |
| 1440 | 1710 | 950 | 279 | 1300 | 671 |
| 1590 | 1710 | 950 | 279 | 1378 | 689 |
| 1740 | 1800 | 1000 | 300 | 1454 | 704 |
| 1920 | 1850 | 1050 | 312 | 1454 | 717 |
| 2100 | 1890 | 1050 | 312 | 1454 | 736 |
| 2280 | 2010 | 1050 | 312 | 1514 | 764 |
| 2460 | 2010 | 1100 | 324 | 1584 | 794 |
| 2640 | 2070 | 1150 | 352 | 1584 | 804 |
| 2850 | 2070 | 1150 | 352 | 1650 | 820 |
| 3060 | 2160 | 1200 | 360 | 1650 | 834 |
| 3300 | 2155 | 1200 | 360 | 1650 | 834 |
| 3540 | 2350 | 1200 | 360 | 1850 | 880 |
| 3780 | 2430 | 1350 | 393 | 1850 | 917 |
| 4050 | 2430 | 1350 | 393 | 1926 | 930 |
| 4320 | 2520 | 1400 | 413 | 1926 | 930 |
| 4590 | 2520 | 1400 | 413 | 1926 | 931 |
| 4890 | 2520 | 1400 | 413 | 2000 | 954 |
| 5250 | 2610 | 1450 | 414 | 2000 | 964 |
| 5610 | 2610 | 1450 | 414 | 2060 | 981 |
| 6000 | 2700 | 1500 | 446 | 2060 | 1006 |
| 6450 | 2700 | 1500 | 446 | 2138 | 1028 |
| 6900 | 2790 | 1550 | 456 | 2138 | 1034 |
| 7350 | 2790 | 1550 | 456 | 2138 | 1062 |
| 7800 | 2920 | 1550 | 456 | 2332 | 1126 |
| 8300 | 3060 | 1700 | 510 | 2332 | 1156 |
| 8700 | 3060 | 1700 | 510 | 2332 | 1169 |
| 9300 | 3060 | 1700 | 510 | 2332 | 1188 |
| 9900 | 1700 | 1700 | 510 | 2332 | 1188 |
| 10500 | 1770 | 1770 | 531 | 2440 | 1212 |
| 11100 | 1770 | 1770 | 531 | 2440 | 1237 |
| 11700 | 1770 | 1770 | 531 | 2440 | 1279 |
| 12300 | 1910 | 1910 | 573 | 2632 | 1279 |
| 12900 | 1910 | 1910 | 573 | 2632 | 1316 |
| 13500 | 1910 | 1910 | 573 | 2632 | 1353 |
| 14100 | 1910 | 1910 | 573 | 2632 | 1369 |
| 14700 | 2050 | 2050 | 615 | 2824 | 1369 |
| 15400 | 2050 | 2050 | 615 | 2824 | 1387 |
| 16100 | 2050 | 2050 | 615 | 2824 | 1387 |
| 16900 | 2120 | 2120 | 636 | 2922 | 1415 |
| 17800 | 2120 | 2120 | 636 | 2922 | 1431 |
| 18800 | 2190 | 2190 | 657 | 3018 | 1461 |
| 20000 | 2190 | 2190 | 657 | 3018 | 1493 |
| 26000 | 2360 | 2360 | 716 | 3258 | 1628 |

Type M Spek Anchor

Type M Spek Anchor

Specifications

| Nominal Weight (KG) | Size(mm) |
| --- | --- |
|  | A | B | C | D | E | H |
| 80 | 339 | 468 | 108 | 611 | 336 | 222 |
| 105 | 371 | 512 | 120 | 669 | 336 | 242 |
| 135 | 371 | 512 | 149 | 669 | 368 | 254 |
| 180 | 445 | 613 | 142 | 800 | 440 | 290 |
| 240 | 445 | 613 | 182 | 800 | 440 | 304 |
| 300 | 527 | 727 | 168 | 949 | 522 | 344 |
| 360 | 527 | 727 | 190 | 949 | 522 | 358 |
| 420 | 590 | 813 | 188 | 1062 | 584 | 385 |
| 480 | 590 | 813 | 211 | 1062 | 584 | 395 |
| 570 | 652 | 900 | 208 | 1175 | 647 | 428 |
| 660 | 653 | 900 | 236 | 1175 | 647 | 438 |
| 780 | 725 | 1000 | 231 | 1305 | 718 | 473 |
| 900 | 725 | 1000 | 264 | 1215 | 718 | 485 |
| 1020 | 793 | 1093 | 252 | 1428 | 785 | 518 |
| 1140 | 793 | 1093 | 277 | 1428 | 785 | 530 |
| 1290 | 858 | 1183 | 273 | 1544 | 850 | 561 |
| 1440 | 858 | 1183 | 299 | 1544 | 850 | 573 |
| 1590 | 920 | 1268 | 293 | 1655 | 911 | 604 |
| 1740 | 920 | 1268 | 315 | 1655 | 911 | 611 |
| 1920 | 980 | 1350 | 312 | 1761 | 970 | 640 |
| 2100 | 980 | 1350 | 337 | 1761 | 970 | 650 |
| 2280 | 1038 | 1430 | 331 | 1866 | 1027 | 678 |
| 2460 | 1038 | 1430 | 355 | 1866 | 1027 | 688 |
| 2640 | 1090 | 1500 | 347 | 1959 | 1079 | 712 |
| 2850 | 1190 | 1500 | 380 | 1950 | 1079 | 722 |
| 3060 | 1144 | 1578 | 365 | 2058 | 1133 | 748 |
| 3300 | 1144 | 1578 | 387 | 2058 | 1133 | 760 |
| 3540 | 1202 | 1656 | 383 | 2159 | 1189 | 785 |
| 3780 | 1202 | 1656 | 405 | 2159 | 1189 | 787 |
| 4050 | 1257 | 1732 | 400 | 2258 | 1244 | 821 |
| 4320 | 1257 | 1732 | 422 | 2258 | 1244 | 831 |
| 4590 | 1257 | 1732 | 444 | 2258 | 1244 | 841 |
| 4890 | 1338 | 1846 | 426 | 2405 | 1325 | 874 |
| 5250 | 1338 | 1846 | 450 | 2405 | 1325 | 888 |
| 5610 | 1432 | 1974 | 431 | 2405 | 1418 | 936 |
| 6000 | 1432 | 1974 | 457 | 2577 | 1418 | 936 |
| 6450 | 1432 | 1974 | 483 | 2577 | 1418 | 950 |
| 6900 | 1533 | 2112 | 462 | 2757 | 1518 | 1001 |
| 7350 | 1533 | 2112 | 488 | 2757 | 1518 | 1001 |
| 7800 | 1533 | 2112 | 514 | 2757 | 1518 | 1015 |
| 8300 | 1621 | 2234 | 489 | 296 | 1605 | 1059 |
| 8700 | 1621 | 2234 | 517 | 2916 | 1605 | 1059 |
| 9300 | 1621 | 2234 | 545 | 2916 | 1605 | 1074 |
| 9900 | 1726 | 2380 | 520 | 3015 | 1709 | 1128 |
| 10500 | 1726 | 2380 | 550 | 3105 | 1709 | 1128 |
| 11100 | 1726 | 2380 | 580 | 3105 | 1709 | 1138 |
| 11700 | 1819 | 2507 | 554 | 3273 | 1701 | 1188 |
| 12300 | 1819 | 2507 | 580 | 3273 | 1701 | 1188 |
| 12900 | 1819 | 2507 | 607 | 3273 | 1701 | 1200 |
| 13500 | 1904 | 2624 | 577 | 3425 | 1885 | 1243 |
| 14100 | 1904 | 2624 | 607 | 3425 | 1885 | 1243 |
| 14700 | 1904 | 2624 | 650 | 3425 | 1885 | 1243 |
| 15400 | 1904 | 2782 | 657 | 3425 | 1885 | 1263 |
| 16100 | 2018 | 2782 | 612 | 3632 | 1998 | 1318 |
| 16900 | 2018 | 2782 | 638 | 3632 | 1998 | 1318 |
| 17800 | 2018 | 2782 | 683 | 3632 | 1998 | 1318 |
| 18800 | 2018 | 2782 | 699 | 3632 | 1998 | 1343 |
| 20000 | 2170 | 2990 | 652 | 3905 | 2148 | 1416 |

Type SR Spek Anchor

Type SR Spek Anchor Drawing

Specification

| Nominal Weight(kg) | Size(mm) |
| --- | --- |
|  | A | B | B1 | G |
| 210 | 810 | 500 | 340 | 690 |
| 240 | 810 | 500 | 340 | 690 |
| 300 | 980 | 550 | 390 | 760 |
| 360 | 970 | 600 | 412 | 828 |
| 420 | 970 | 600 | 412 | 828 |
| 450 | 970 | 600 | 412 | 828 |
| 480 | 970 | 650 | 442 | 900 |
| 570 | 1050 | 650 | 442 | 900 |
| 610 | 1050 | 700 | 472 | 962 |
| 660 | 1134 | 700 | 472 | 962 |
| 750 | 1134 | 750 | 508 | 1032 |
| 780 | 1215 | 750 | 519 | 1032 |
| 900 | 1215 | 800 | 547 | 1100 |
| 980 | 1296 | 800 | 547 | 1100 |
| 1020 | 1296 | 850 | 573 | 1170 |
| 1040 | 1377 | 900 | 591 | 1240 |
| 1100 | 1458 | 900 | 620 | 1240 |
| 1200 | 1458 | 950 | 640 | 1300 |
| 1300 | 1539 | 950 | 640 | 1300 |
| 1400 | 1539 | 950 | 671 | 1300 |
| 1500 | 1539 | 950 | 671 | 1300 |
| 1650 | 1620 | 1000 | 669 | 1378 |
| 1800 | 1700 | 1050 | 704 | 1454 |
| 1920 | 1700 | 1050 | 717 | 1454 |
| 2100 | 1700 | 1050 | 136 | 1454 |
| 2190 | 1700 | 1050 | 736 | 1454 |
| 2280 | 1782 | 1100 | 764 | 1584 |
| 2460 | 1863 | 1150 | 794 | 1484 |
| 2640 | 1863 | 1150 | 804 | 1584 |
| 2850 | 1944 | 1200 | 812 | 1650 |
| 3300 | 1944 | 1200 | 834 | 1650 |
| 3540 | 1944 | 1200 | 834 | 1650 |
| 3780 | 2187 | 1350 | 880 | 1850 |
| 4050 | 2187 | 1350 | 914 | 1850 |
| 4320 | 2268 | 1400 | 917 | 1926 |
| 4590 | 2268 | 1400 | 931 | 1926 |
| 4890 | 2268 | 1400 | 954 | 1926 |
| 5250 | 2349 | 1450 | 964 | 2000 |
| 5610 | 2349 | 1450 | 981 | 2000 |
| 5800 | 2430 | 1500 | 1006 | 2060 |
| 6000 | 2430 | 1500 | 1006 | 2060 |
| 6450 | 2430 | 1500 | 1023 | 2060 |
| 6900 | 2510 | 1550 | 1034 | 2138 |
| 7350 | 2510 | 1550 | 1062 | 2138 |
| 7800 | 2510 | 1550 | 1091 | 2138 |
| 8000 | 2510 | 1550 | 1091 | 2138 |
| 8300 | 2754 | 1700 | 1125 | 2332 |
| 8700 | 2754 | 1700 | 1166 | 2332 |
| 9300 | 2754 | 1700 | 1188 | 2332 |
| 9900 | 2754 | 1700 | 1188 | 2332 |
| 10500 | 2867 | 1770 | 1197 | 2440 |
| 11100 | 2867 | 1770 | 1212 | 2440 |
| 11700 | 2867 | 1770 | 1237 | 2440 |
| 12300 | 3094 | 1910 | 1260 | 2632 |
| 12900 | 3094 | 1910 | 1260 | 2632 |
| 13500 | 3094 | 1910 | 1316 | 2632 |
| 14700 | 3321 | 2050 | 1369 | 2824 |
| 16900 | 3434 | 2120 | 1415 | 2922 |
| 18800 | 3548 | 2190 | 1461 | 3018 |
| 20000 | 3548 | 2190 | 1493 | 3018 |

Contact Us

Company Name:

Chongqing Hi-Sea Marine Equipment Import & Export Co.,Ltd.

Address:

15-1, Jinshan Matrix A, Saidi Rd., New North Zone, Chongqing 401122, China

Telphone:

+86-23-67868920, 67956606

Fax:

+86-23-67956622

E-mail:

manager@hiseamarine.com,  sales3@hiseamarine.com

Website:

www.hiseamarine.com